## Slide 1
PrempehTech
MAC Addresses
Beginner Networking Lesson
What a MAC address is, how it looks, and why we use it

## Slide 2
2. What Is a MAC Address?
PrempehTech
MAC stands for Media Access Control.
A MAC address is a Layer 2 address associated with a network interface.
It helps identify an interface during communication on a local network.
Example: 00:1A:2B:3C:4D:5E

## Slide 3
3. Which Devices Have MAC Addresses?
PrempehTech
Laptop → technically, its Wi-Fi/Ethernet interface has the MAC address.
Phone → its Wi-Fi interface has a MAC address.
Router → its individual Ethernet/Wi-Fi interfaces can have MAC addresses.
VM → its virtual NIC has a MAC address.
Switch → its own relevant interfaces/logical interfaces can have MAC addresses.
Important: the MAC address is associated with the network interface, not simply the whole device.

## Slide 4
4. Special MAC Addresses
PrempehTech
Not every MAC address identifies one individual interface.
Some MAC addresses are special addresses used for particular types of communication.
Ethernet broadcast address:
FF:FF:FF:FF:FF:FF
This address represents a broadcast to devices on the local Layer 2 network.

## Slide 5
5. MAC Address Size
PrempehTech
A standard MAC address is 48 bits long.
48 bits = 6 bytes.
It is usually written as 12 hexadecimal digits.
00 : 1A : 2B : 3C : 4D : 5E
Each pair represents one byte.

## Slide 6
6. Hexadecimal in a MAC Address
PrempehTech
Hexadecimal uses 16 symbols: 0–9 and A–F.
One hexadecimal digit represents 4 bits.
Two hexadecimal digits represent 8 bits = 1 byte.
That is why a 6-byte MAC address is commonly written using 12 hexadecimal digits.

## Slide 7
7. Manufacturer Portion
PrempehTech
A traditional manufacturer-assigned MAC address contains an organization/manufacturer portion.
Example for learning:
00:1A:2B : 3C:4D:5E
The first 3 bytes are traditionally associated with the organization/manufacturer assignment.
The remaining 3 bytes help identify the individual interface within that assignment.

## Slide 8
8. MAC Address vs IP Address
PrempehTech
MAC address and IP address are not the same thing.
MAC example: 00:1A:2B:3C:4D:5E
IP example: 192.168.1.10
For now: MAC is a Layer 2 address; IP is a Layer 3 logical address.
We will connect these ideas more deeply in later lessons.

## Slide 9
9. MAC Address in an Ethernet Frame
PrempehTech
In Part 3, we learned that Ethernet uses frames.
An Ethernet frame contains a source MAC address.
It also contains a destination MAC address.
Source MAC → where the frame came from on the local link.
Destination MAC → where the frame is being sent on the local link.

## Slide 10
10. Find a MAC Address
PrempehTech
Windows:
Open Command Prompt and run: ipconfig /all
Look for: Physical Address
Wireshark:
Expand Ethernet II and look at Source and Destination.
This lets us see MAC addresses in real network traffic.

## Slide 11
11. MAC Address Recap
PrempehTech
MAC = Media Access Control.
A standard MAC address is 48 bits = 6 bytes.
MAC addresses are normally written in hexadecimal.
MAC addresses are generally associated with network interfaces.
Manufacturer-assigned MAC addresses traditionally contain an organization/manufacturer portion.
Special addresses also exist, such as FF:FF:FF:FF:FF:FF for Ethernet broadcast.
Next lesson: ARP.